## Slide 1: PIF
Input from Netronome:
- IR Additions for P4
- Run-Time Interface Considerations

## Slide 2: iNIC P4 + PIF IR Implementation: Compilation + Development Environment
app.P4
Compile / Link
app.firmware
plugin.C
Stateful / complex
packet processing code
Parse - Match - Act
Dataplane Program
Native code
for NFP iNIC
Network
app.IR
Compile
Intermediate Representation
ONF PIF => OpenSourceSDN.org
P4 and C Integrated
Development
Environment
Edit - Build - Run
=
Debug
Run-time interaction

## Slide 3: Goals + Approach
Compile to Netronome Network Flow Processor native code
Support both P4 high level language and OSSDN IR (AIR-IRI)
  Leverage existing P4.org high level language compiler
  Translate P4 “HLIR” (Python objects in memory) to AIR-IRI (objects in YAML file)
Alignment between HLIR and AIR-IRI
  Some constructs align well e.g. header definitions, parsing, control flow
  Added constructs not covered yet
Added mechanisms for IDE integration and run-time interface

## Slide 4: IR Additions for Parsing
Setting metadata within parse node
  Added “sets” key with array metadata refs
Value + Mask select values
  Tagged transition with optional mask field: start -> parse_ethernet [value=0xdead, mask=0xffff]
Variable control flow entry point
  Parser can 'jump' to any node in ingress/egress flow

## Slide 5: IR Additions for Control Flow
Conditional transition based on field values/header valid _condition_0: type : conditional format : pyexpr condition : (ingress_metadata.ingress_bypass == 0x0)
In digraph _condition_0 -> exit_control_flow [condition = false]

## Slide 6: IR Additions for Registers + Counters
Instantiation: cntr_direct: type : register class : global table : tbl_testval_0 instance_count : 4 fields : - value_bytes : 48 - value_packets : 32 counts : - bytes : value_bytes - packets : value_packets
Action: count(cntr_global.value_packets, 1); count_bytes(cntr_global.value_packets, 0); register_read(test_metadata.val32, cntr_global.value_packets) register_write(cntr_global.value_packets, 0)
Notes:
  Registers and counters are declared in the same way
  Counters have the addition 'counts' property

## Slide 7: IR Additions for Digests (Events)
Instantiation: test_event_field_list: type : field_list fields : - ethernet.dstAddr - test_metadata.val0 - test_metadata.val1 test_event : type : digest identifier : 1 field_list : test_event_field_list
Action: generate_digest(test_event);

## Slide 8: IR Additions for Header Stacks
Instantiation: vlan : type : header max_depth : 5 fields : - pcp : 3 - cfi : 1 - vid : 12 - etherType : 16
Action: remove_header(vlan[1]); pop(vlan, 2); remove_header(vlan[last]);
Control flow: valid(vlan[0]) vlan[1].vid vlan[last].vid

## Slide 9: IR Additions for Development Environment
Source info section: date, revision strings, source files, output file name... source_info : type : source_info date : 2015-06-30 09:03:35 source_files : ...
Source filename and line number per object
  Allows mapping AIR-IRI output to original P4 source

## Slide 10: iNIC P4 + PIF IR Implementation: Run-Time Interaction
app.firmware
Native code
for NFP iNIC
Network
Debug
Debug API
Callable API
e.g. Thrift
VNF or L4-L7
or other app
table_data.JSON
Generated CLI
vs API driven CLI
Toolchain
OpenFlow
Agent
SDN
Controller
OpenFlow ++
API
table_info.JSON
Describe tables, action data
=> generated model (TTP )?
Vendor specific
e.g. memory layout

## Slide 11: Run-time Interface Details
Workflow options
  Create model (~ .h file), then write program (~ .c file) to conform
  Create program, then extract interface (model, API…) from it
Generated items
  Model
    Consumed by tools, controller etc.
    Negotiated too?
  Interface
    Example: “IDL” for Thrift => callable API (C, Python…)
  Vendor/implementation specific debug info
Schema and encoding of items can be discussed
  Prototype: model in purpose specific JSON format
  Create Table Typing Pattern (TTP), or new instance of Negotiable Datapath Model (NDM)?